## Slide 1: Data Explanation
Neural Engineering – SP25
Alex Mikhael
Prof. Jose del.R Millan

## Slide 2: TASK DESIGN – NBACK
Numbers (0-9), N = 2
1 Trial :
+
1500 ms
Baseline
NBack
7 runs  N =2
25 trials / run, 175 trials/block in total
1
500 ms
+
600 ms
Subject can respond
Button press (Z : No, M : Yes)

## Slide 3
NBACK TRAINING
+
GEL
5 blocks
50 trials/block
N = 2
tACS/
control
20 minutes
2 mA
NBACK
Offline
8 blocks
50 trials/block
N = 2
EC
Rest
Eyes closed 2 min
Get tACS taget frequency
tACS and Nback task
NBACK
Offline
2 min
EC
2 min
Day 1
tACS/
control
20 minutes
2 mA
4 blocks
50 trials/block
N = 2
EC
2 min
EC
2 min
Day 2
NBACK
+
BCI
NBACK
+
BCI
NBACK
+
BCI

## Slide 4: Files
Each student will have 1 folder with their subject ID on it containing :
  Nback task data before tACS : ses-S001N2pre
  Eyes closed data before tACS : ses-S001ecpre
  Nback task data after tACS : ses-S001N2post
  Eyes closed data after tACS : ses-S001ecpost
ch32Locations.mat : channels location/name for the EEG data

## Slide 5: Data Format
Eyes closed and Eyes open data will contain :
  EEG data
Nback data will contain :
  1 stream with 2 cells
  Each cell contains : info (MarkerStream for the markers (explained next slide) and EEG/EOG for the data)
  time_series : Markers data or EEG data
  time_stamps : time vector
  You can find additional information in the streams (sampling rate, channel names, …)
EEG data is in the first 32 channels in the EEG stream
EOG data is in “AUX 7”, “AUX 8” channels
Hint : If you are using matlab, load the data using streams = loadxdf(…) function

## Slide 6: Marker Stream
The following values indicate :
  0 : Trial start
  100 : Button press + match (subject answered yes)
  200 : Button press + non-match (subject answered no)
  300 : Timeout (subject did not answer in time)
  400 : Trial end
  1 : Correct trial
  2 : Incorrect trial
  11 : Match trials
  12 : Non-match trials
In the marker stream, each marker value is paired with the corresponding timestamp